AUTO WORLD SUBDIVISION

Engineering Comments: Must comply with the Mobile County Flood Damage Prevention Ordinance. Development shall be designed to comply with the storm water detention and drainage facility requirements of the City of Mobile storm water and flood control ordinances, and requiring submission of certification from a licensed engineer certifying that the design complies with the storm water detention and drainage facility requirements of the City of Mobile storm water and flood control ordinances prior to the issuance of any permits

Fire-Rescue Department Comments:  Subdivision layout and design must comply with the requirements of the 2003 International Fire Code, including Appendices B through D, as adopted by the City of Mobile.  Commercial buildings and sites within the City of Mobile Fire Jurisdiction must comply with the requirements of the 2003 International Fire Code, including Appendices B through D, as adopted by the City of Mobile, and the 2003 International Existing Building Code, as appropriate.

MAWSS Comments:  No comments submitted.

The plat illustrates the proposed 4 lot, 11.9+ acres subdivision located on the North side of Tanner Williams Road, 245’+ East of Tanner Williams Court, within the planning jurisdiction.  The subdivision is served by public water and sanitary services.

The purpose of this application is to create four legal lots from six existing metes-and-bounds parcels.

The site fronts on Tanner Williams Road which is a component of the Major Street Plan with a planned 100’ right-of-way.  The plat indicates a varying right of way width along the subject site; therefore, the plat should be revised to indicate the current right-of-way width along the site with the dedication of sufficient right-of-way to provide 50’ from the centerline of Tanner Williams Road if not currently that.

No building setback line is indicated on the plat; therefore the plat should be revised to indicate a 25’ minimum building setback line along all four lots where they front Tanner Williams Road with the setback measured from any required right-of-way dedication.  Proposed Lot 3 is an expansion of Lot 2, Larry & Bradley Ward Subdivision, a previous submittal by the applicant, which indicates a 45’ minimum building setback along Tanner Williams Road.  That plat indicates a 60’ right-of-way on Tanner Williams Road, and the building setback allowed for a future 100’ right-of-way with a 25’ setback from the future right-of-way line.  No dedication was required with the approval of that subdivision in 1999, but since the site is primarily commercial, current policy is to require dedication depending on the verified right-of-way width.  Also, since proposed Lot 3 fronts the rear of proposed Lots 1, 2 and 4, and the rear of Lot 1, Larry & Bradley Ward Subdivision, it would be appropriate for the 25’ minimum building setback line for Lot 3 to be measured from the rear line of those four properties, and should be so-indicated on the final plat.

As a means of access management, a note should be required on the final plat stating that each lot is limited to one curb cut to Tanner Williams Road, with the size, location and design to be approved by County Engineering and conform to AASHTO standards.

Each lot is labeled with its size in square feet and the plat should be revised to label each lot with its size in square feet and acreage, or a table should be furnished on the plat providing the same information.

According to Section V.D.3 of the Subdivision Regulations, the maximum depth of any lots shall not be more than 3.5 times the width of the lot at the building setback line.  While proposed Lots 1, 2 and 3 would exceed this ratio, this is typical of other metes-and bounds lots in the immediate neighborhood, and typical of Lot 2 of the previously mentioned Larry & Bradley Ward Subdivision, and typical of a lot across Tanner Williams Road in another subdivision, Ward Enterprises Subdivision, submitted by the applicant and approved by the Commission in 2004.  Proposed Lot 3 would be an expansion of Lot 2 (a flag lot), of Larry & Bradley Ward Subdivision.  The April 2008 amendment to Section V.D.1. of the Subdivision Regulations generally does not allow the creation of panhandle or flag lots.  While the creation of flag lots is discouraged, they are permitted only in those locations where varied and irregularly-shaped lot designs are common and the informality of design is consistent with other lots in the vicinity; or, where unusual circumstances such as an odd shaped lot exists; or, separate disparate uses exist on a single lot.  Proposed Lot 3 would be consistent with the two previously approved subdivisions submitted by the applicant, and would serve to consolidate most of the applicant’s junk yard operations onto one lot.  Therefore, a waiver of Sections V.D.1. and  V.D.3. of the Subdivision Regulations would be justified.

While the site is in Mobile County, it will have to comply with the City of Mobile storm water and flood control ordinances.  A note should be placed on the final plat stating that the development will be designed to comply with the storm water detention and drainage facility requirements of the City of Mobile storm water and flood control ordinances, and requiring submission of certification from a licensed engineer certifying that the design complies with the storm water detention and drainage facility requirements of the City of Mobile storm water and flood control ordinances prior to the issuance of any permits.  Certification is to be submitted to the Planning Section of Urban Development and County Engineering.

The geographic area defined by the City of Mobile and its planning jurisdiction, including this site, may contain Federally-listed threatened or endangered species as well as protected non-game species.  Development of the site must be undertaken in compliance with all local, state and Federal regulations regarding endangered, threatened or otherwise protected species.

A note should be placed on the Final Plat stating that any lots which are developed commercially and adjoin residentially developed property must provide a buffer, in compliance with Section V.A.7. of the Subdivision Regulations.

With a waiver of Sections V.D.1. and V.D.3., the proposed plat meets the minimum requirements of the Subdivision Regulations and is recommended for tentative approval subject to the following conditions:

- revision of the plat to indicate the current right-of-way width along Tanner Williams Road, and dedication of sufficient right-of-way to provide 50’ from the centerline of Tanner Williams Road, if currently less;

- illustration of the 25’ minimum building setback line along Tanner Williams Road for all lots, as measured from any required dedicated right-of-way;

- illustration of a 25’ minimum building setback line on Lot 3 from the rear line of Lots 1, 2 and 4, and the rear line of Lot 1, Larry & Bradley Ward Subdivision;

- placement of a note on the final plat stating  that each lot is limited to one curb cut to Tanner Williams Road, with the size, location and design to be approved by County Engineering and conform to AASHTO standards;

- revision of the plat to label each lot with its size in square feet and acreage, or the furnishing of a table on the plat providing the same information;

- placement of a note on the final plat stating that the development will be designed to comply with the storm water detention and drainage facility requirements of the City of Mobile storm water and flood control ordinances, and requiring submission of certification from a licensed engineer certifying that the design complies with the storm water detention and drainage facility requirements of the City of Mobile storm water and flood control ordinances prior to the issuance of any permits.  Certification is to be submitted to the Planning Section of Urban Development and County Engineering.

- placement of a note on the final plat stating that development of the site must be undertaken in compliance with all local, state and Federal regulations regarding endangered, threatened or otherwise protected species; and

- placement of a note on the final plat stating that any lots which are developed commercially and adjoin residentially developed property must provide a buffer, in compliance with Section V.A.7. of the Subdivision Regulations.