GILL CREEK PLACE SUBDIVISION

Engineering Comments: Must comply with the Mobile County Flood Damage Prevention Ordinance.

The plat illustrates the proposed 1 lot, 11.0 + acres subdivision which is located on the East side of McDonald Road, 1/3 mile + South of Holloway Drive North.  The subdivision is served by public water and individual septic systems.

The purpose of this application is to create a one-lot subdivision from a metes and bounds parcel.

McDonald Road, which has an existing right-of-way of 60-feet, is shown as a major street on the Major Street Plan, and as such requires a 100-foot right-of-way; therefore, only one lot need additional setback, not dedication of sufficient right-of-way to provide 50-feet from the centerline should be required.  Additionally, as a means of access management, a note should be placed on the final plat stating that the site is limited to one curb cut to McDonald Road, should be required.

There is a triangular shaped parcel which is excluded from the property.  This triangle was deeded off in 1994 and the participants in this transaction no longer own the property; and based upon Planning Commission practice this triangle may be excluded from the final plat.

This site is located in the County, thus a note should be placed on the final plat stating that any lots which are developed commercially and adjoin residentially developed property must provide a buffer, in compliance with Section V.A.7. of the Subdivision Regulations.

The 25-foot minimum building setback line is not shown but would be required on the final plat.

The plat meets the minimum requirements of the Subdivision Regulations and is recommended for Tentative Approval subject to the following conditions: 1) the placement of a note on the final plat stating that the site is limited to two curb cuts to McDonald Road, with the size, location and design to be approved by County Engineering; 2) the placement of a note on the final plat stating that any lots which are developed commercially and adjoin residentially developed property must provide a buffer, in compliance with Section V.A.7. of the Subdivision and 3) the placement of the 25-foot minimum setback line on the final plat.